## Slide 1: UNIT-V
Embedded Linux
07 Hours

## Slide 2
CONTENTS
Need of Linux
Embedded Linux Today
Open Source and the GPL
BIOS Versus Boot loader
Cross- Development Environment
Host System Requirements
Hosting Target Boards
Development Tools
GNU Debugger
Tracing and Profiling Tools
Binary Utilities
Role of a Boot loader
Boot loader Challenges
Device Driver Concepts
Module Utilities
Driver Methods
Linux File System & Concepts

## Slide 3
Embedded Linux
Linux® is an open source operating system (OS).
Embedded Linux is a type of Linux operating system/kernel that is designed to be installed and used within embedded devices and appliances.
It is a compact version of Linux that offers features and services in line with the operating and application requirement of the embedded system.
Linux has been adopted for embedded products in the worldwide public switched telephone network, global data networks, wireless cellular handsets, and the equipment that operates these networks.
Linux has enjoyed success in automobile applications, consumer products such as games and PDAs, printers, enterprise switches and routers, and many other products.

## Slide 4
Embedded Linux is a type of Linux operating system/kernel that is designed to be installed and used within embedded devices and appliances.
It is a compact version of Linux that offers features and services in line with the operating and application requirement of the embedded system.

## Slide 5
Need of Linux
Some of the reasons for the growth of embedded Linux are as follows:
Linux has emerged as a mature, high-performance, stable alternative to traditional proprietary embedded operating systems.
Linux supports a huge variety of applications and networking protocols.
Linux is scalable, from small consumer-oriented devices to large, heavy-iron, carrier-class switches and routers.
Linux can be deployed without the royalties required by traditional proprietary embedded operating systems.
Linux has attracted a huge number of active developers, enabling rapid support of new hardware architectures, platforms, and devices.
An increasing number of hardware and software vendors, including virtually all the top-tier manufacturers and ISVs, now support Linux.

## Slide 6
For these and other reasons, there is huge adoption of Linux in many common household items, ranging from high-definition television sets to cellular handsets.

## Slide 7
Embedded Linux Today
Linux has experienced significant growth in the embedded space.
It is difficult to estimate the market size of Linux because many companies still build their own embedded Linux distributions.
LinuxDevices.com, the popular news and information portal founded by Rich Lehrbaum, conducts an annual survey of the embedded Linux market.
In its latest survey, they report that Linux has emerged as the dominant operating system used in thousands of new designs each year.
In fact, nearly half of respondents reported using Linux in an embedded design, while the nearest competing operating system was reportedly used by only about one in every eight respondents.
Commercial operating systems that once dominated the embedded market were reportedly used by fewer than one in ten respondents.
Even if you find reason to dispute these results, no one can ignore the momentum in the embedded Linux marketplace today.

## Slide 8
Open Source and the GPL
One of the fundamental factors driving the adoption of Linux is the fact that it is open source.
The Linux kernel is licensed under the terms of the GNU GPL[1] (General Public License), which leads to the popular myth that Linux is free.[2]
In fact, the second paragraph of the GNU GPL declares:
"When we speak of free software, we are referring to freedom, not price." The GPL license is remarkably short and easy to read.
.

## Slide 9
No matter how the software was obtained, the GPL grants the licensee unlimited distribution rights, without the obligation to pay royalties or per-unit fees.
This does not mean that a vendor can't charge for the GPL software this is a very reasonable common business practice.
It means that once in possession of GPL software, it is permissible to modify and redistribute it, whether it is a derived (modified) work or not.
However, as defined by the GPL license, the author(s) of the modified work are obligated to release the work under the terms of the GPL if they decide to do so.
Any distribution of a derived work, such as shipment to a customer, triggers this obligation.
For a fascinating and insightful look at the history and culture of the open source movement, read Eric S. Raymond's book referenced at the end of this chapter.

## Slide 10
Among the most important key characteristics:
The license is self-perpetuating.
The license grants the user freedom to run the program.
The license grants the user the right to study and modify the source code.
The license grants the user permission to distribute the original code or his modifications.
The license grants these same rights to anyone to whom you distribute GPL software.

## Slide 11
When a software work is released under the terms of the GPL (General Public License), it must forever carry that license.[3]
Even if the code is highly modified, which is allowed and even encouraged by the license, the GPL mandates that it must be released under the same license.
The intent of this feature is to guarantee access to everyone, even of modified versions of the software (or derived works, as they are commonly called).

## Slide 12
Linux is Embedded or Not?
Several key attributes are usually associated with embedded systems.
Embedded systems come in a variety of shapes and sizes, from the largest multiple-rack data storage or networking powerhouses to tiny modules such as your personal MP3 player or your cellular handset.
Some of the usual characteristics of embedded systems include these:

## Slide 13
Contain a processing engine, such as a general-purpose microprocessor
Typically designed for a specific application or purpose Includes a simple (or no) user interface an automotive engine ignition controller, for example
Often is resource limited for example, has a small memory footprint and no hard drive
Might have power limitations, such as a requirement to operate from batteries
Usually is not used as a general-purpose computing platform Generally has application software built in, not user selected
Ships with all intended application hardware and software pre-integrated Often is intended for applications without human intervention
Most commonly, embedded systems are resource constrained compared to the typical desktop PC.
Embedded systems often have limited memory, small or no hard drives, and sometimes no external network connectivity.
Frequently, the only user interface is a serial port and some LEDs.
These and other issues can present challenges to the embedded system developer.

## Slide 14
BIOS Versus Boot loader
When power is first applied to the desktop computer, a software program called the BIOS immediately takes control of the processor.
(Historically, BIOS -Basic Input/Output Software, but the now its functionality have become much more complex.
The BIOS is a complex set of system-configuration software routines that have knowledge of the low- level details of the hardware architecture.
The BIOS first gains control of the processor when power is applied.
Its primary responsibility is to initialize the hardware, especially the memory subsystem, and load an operating system from the PC's hard drive.

## Slide 15
Bootloader
In a typical embedded system a boot loader is the software program that performs these same functions as BIOS does,.
In your own custom embedded system, part of your development plan must include the development of a bootloader specific to your board.
Luckily, several good open source bootloaders are available that you can customize for your project.

## Slide 16
Some of the more important tasks that your bootloader performs on power-up are as follows:
Initializes critical hardware components, such as the SDRAM controller, I/O controllers, and graphics controllers
Initializes system memory in preparation for passing control to the operating system
Allocates system resources such as memory and interrupt circuits to peripheral controllers, as necessary
Provides a mechanism for locating and loading your operating system image
Loads and passes control to the operating system, passing any required startup information that might be required, such as total memory size clock rates, serial port speeds and other lowlevel hardware specific configuration data

## Slide 17
The important point to remember is this:
If your embedded system will be based on a custom designed platform, these bootloader functions must be supplied by you, the system designer.
If your embedded system is based on a commercial off-the-shelf (COTS) platform such as an ATCA chassis, typically the bootloader (and often the Linux kernel) is included on the board.

## Slide 18
Typical Embedded Linux Setup
A host development system, running your favorite desktop Linux distribution, such as Red Hat or SuSE or Debian Linux.
Our embedded Linux target board is connected to the development host via an RS-232 serial cable

## Slide 19
We plug the target board's Ethernet interface into a local Ethernet hub or switch, to which our development host is also attached via Ethernet.
The development host contains your development tools and utilities along with target files normally obtained from an embedded Linux distribution.
For this example, our primary connection to the embedded Linux target is via the RS-232 connection.
A serial terminal program is used to communicate with the target board.
Minicom is one of the most commonly used serial terminal applications and is available on virtually all desktop Linux distributions.

## Slide 20
Cross- Development Environment
Cross-platform development is the practice of developing software products or services for multiple platforms or software environments.
A development environment in software and web development is a workspace for developers to make changes without breaking anything in a live environment.
Engineers and developers use various methods to accommodate different operating systems or environments for one application or product.

## Slide 21
Developing software in a cross-development environment requires that the compiler running on your development host gives output as a binary executable file that is incompatible with the desktop development workstation on which it was compiled.
The primary reason these tools exist is that it is often
impractical or impossible to develop and compile software natively on the embedded system because of resource (typically memory and CPU strength) constraints.
A cross-development configuration can develop software for a different target machine than the development tools themselves (which run on the host)-
for example, a SPARCstation can generate and debug code for a Motorola Power PC-based board.

## Slide 22
Host System Requirements
The host is the computer on which you do your development work.
Your development workstation must include several important components and systems.
Of course, you need a properly configured cross tool-chain.
You can download and compile one yourself or obtain one of the many commercial tool-chains available.
The next major item you need is a Linux distribution targeted for your embedded system architecture.
Wind River Linux 8.0 is designed to run on any host that meets the requirements in this section. These requirements assume that the target is a separate computer.

## Slide 23
Your development host requires four separate and distinct capabilities:
Cross tool-chain and libraries
Target system packages, including programs, utilities, and libraries
Host tools such as editors, debuggers, and utilities
Servers for hosting your target board

## Slide 24
If you install a ready-built embedded Linux development environment on your workstation, (either a commercial variety or one freely available in the open source community), the toolchain and components have already been preconfigured to work together.
For example, the toolchain has been configured with default directory search paths that match the location of the target header files and system libraries on your development workstation.
The situation becomes much more complex if your
requirements include having support for multiple architectures and processors on your development
workstation.
This is the reason that embedded Linux distributions exist.

## Slide 25
Hosting Target Boards
Referring back to Figure 12-1 , you will notice an Ethernet connection from the target-embedded board to the host-development system.
Some smaller embedded devices do not have an Ethernet interface.
While developing the kernel, you will compile and download kernels to your embedded board many times.
Many embedded development systems and bootloaders have support for TFTP and assume that the developer will use it.
TFTP is a lightweight protocol for moving files between a TFTP server and TFTP client, similar to FTP.

## Slide 26
TFTP Server is used for simple file transfer (typically for boot-loading remote devices).
Trivial File Transfer Protocol (TFTP) is a simple protocol for exchanging files between two TCP/IP machines.
TFTP servers allow connections from a TFTP Client for sending and receiving files.
Using TFTP from your bootloader to load the kernel will save you countless hours waiting for serial downloads even at higher serial baud rates.
The investment in your time to configure and use TFTP will surely pay off and is highly recommended.
There are very few designs that can't afford the real estate to include an Ethernet port during
development, even if it is depopulated for production.

## Slide 27
Development Tools (Chapter 13 Hallinnan)
A typical embedded Linux distribution includes many useful tools.
Some are complex and some are simple. Some tools might require customization for a particular environment.
This topics presents a cross-section of the most important tools available to the embedded Linux engineer.
A cross-debugger is the debugger itself runs on your development host, but it understands binary executables in the architecture for which it was configured at compile time.

## Slide 28
Tracing and Profiling Tools
Many useful tools can provide you with various views of the system. Some tools offer a high-level perspective, such as what processes are running on your system and which processes are consuming the most CPU bandwidth.
Other tools can provide detailed analysis, such as where memory is being allocated or, even more useful, where it is being leaked.
The next few sections introduce the most important tools and utilities in this category. We have space for only a cursory introduction to these tools; references are provided where appropriate if you want more details.

## Slide 29
GNU Debugger (GDB)
This is a powerful source-level debugging package that lets you see what is going on inside your program.
You can step through the code, set breakpoints, examine and change variables, and so on.
It has a low-level hardware specific debugging support for a wide variety of architectures and microprocessors.
The debugger itself runs on your development host, but it understands binary executables in the architecture for which it was configured at compile time.
The GDB debugger is a complex program with many configuration options during the build process.

## Slide 30
Role of a Boot loader
A boot loader is a critical piece of software running on any system. Whenever a computing system is initially powered on, the first piece of code to be loaded and run is the boot loader. It provides an interface for the user to load an operating system and applications.
The boot loaders reside in the root directory of each Windows partition. Once selected, the boot loaders take over the boot process and load the operating system in accordance with the selected boot parameters
A boot loader is a program that is found by the system BIOS (or UEFI) in the boot sector of your storage device (floppy or hard drive's Master_boot_record), and which locates and starts your operating_system
( Linux ) for you.

## Slide 31
Boot loader Challenges
1 DRAM Controller. DRAM chips cannot be directly read from or written to like other microprocessor bus resources.
2 Flash Versus RAM. ...
3 Image Complexity. ...
4 Execution Context.

## Slide 32
Binary Utilities
The GNU Binary Utilities, or binutils, are a set of programming tools for creating and managing binary programs, object files, libraries, profile data, and assembly source code
Binutils is a collection of software development tools containing a linker, assembler and other tools to work with object files and archives.
Binary utilities, or binutils, are a critical component of any tool-chain.
Indeed, to build a compiler, you must first have successfully built binutils.

## Slide 33
Binutils are cross-utilities and must be built to execute on your development host while operating on binary files targeted to your chosen architecture.

## Slide 34
Device Driver Concepts
(By Hallinan-Embedded-linux-primer Ch 8)
Many real-time operating systems do not have a similar architecture. Hence, Many experienced embedded developers struggle.
The problems occur with introduction of virtual memory and kernel space versus user space i.e. due to complexity.
One of the fundamental purposes of a device driver is to isolate the user's programs from ready access to critical kernel data structures and hardware devices.
Furthermore, a well-written device driver hides the complexity and variability of the hardware device from the user.

## Slide 35
For example, a program that wants to write data to the hard disk need not care if the disk drive uses 512-byte or 1024-byte sectors.
The user simply opens a file and issues a write command.
The device driver handles the details and isolates the user from the complexities and perils of hardware device programming.
The device driver provides a consistent user interface to a large variety of hardware devices.
It provides the basis for the familiar UNIX/Linux convention that everything must be represented as a file.

## Slide 36
Module Utilities
There we used the module utility modprobe to insert and remove a device driver module from a Linux kernel.
A number of small utilities are used to manage device driver modules.
This section introduces them.
You are encouraged to refer to the man page for each utility, for complete details.
In fact, those interested in a greater knowledge of Linux loadable modules should consult the source code for these utilities.

## Slide 37
Driver Methods
We've covered much ground in our short treatment of module utilities.
In the remaining sections of this chapter, we describe the basic mechanism for communicating with a device driver from a user space program (your application code).
We have introduced the two fundamental methods responsible for one-time initialization and exit processing of the module.
Recall from Listing 8-1 that these are module_init() and module exit().
We discovered that these routines are invoked at the time the module is inserted into or removed from a running kernel.

## Slide 38
Now we need some methods to interface with our device driver from our application program.
After all, two of the more important reasons we use device drivers are to isolate the user from the perils of writing code in kernel space and to present a unified method to communicate with hardware or kernel-level devices.

## Slide 39
Linux File System & Concepts
Before delving into the details of the individual file systems.
let's look at the big picture of how data is stored on a Linux system.
In our study of device drivers in Chapter 8, "Device Driver Basics," we looked at the structure of a character device.
In general, character devices store and retrieve data in serial streams.
The most basic example of a character device is a serial port or magnetic tape drive.
In contrast, block devices store and retrieve data in equal-sized chucks of data at a time.

## Slide 40
For example, a typical IDE hard disk controller can transfer 512 bytes of data at a time to and from a specific, addressable location on the physical media.
File systems are based on block devices.
Loadable Modules:
In Linux, device driver modules can be added or removed dynamically after boot time.
Loadable modules enhance field upgrade capabilities. For example, the module itself can be updated in a live system without the need for a reboot

## Slide 41
Loadable modules have particular importance to embedded systems.
Loadable modules enhance field upgrade capabilities; the module itself can be updated in a live system without the need for a reboot.
Modules can be stored on media other than the root (boot) device, which can be space constrained.

## Slide 42
Device Driver Architecture
The basic Linux device driver model is familiar to UNIX/Linux system developers.
Device drivers are broadly classified into two basic categories: character devices and
block devices.
Character devices can be thought of as serial streams of sequential data.
Examples - serial ports and keyboards.
Block devices are characterized by the capability to read and write blocks of data to and from random locations on an addressable medium.
Examples of block devices include hard drives and floppy disk drives.